%varphi_1 ( t ) %varphi_2 ( t ) bar a_B ^%tau bar a_B ^n bar v_B A B C bar a_{C/B} ^n bar a_{C/B} ^n bar v_{C/B} Mechanical Analysis

Velocity and Acceleration of Mechanical Finger

y

x
z

left lbrace alignl { binom {V_B % = % %omega _1(t) l_AB} {V_{C/B} % = % %omega _2(t) l_BC} } right none left lbrace alignl { binom {a_B ^%tau % = % %varepsilon _1(t) l_AB} {a_B ^ n% = % %omega_1^2(t) l_AB} } right none left lbrace alignl { binom {a_{C/B} ^%tau % = % %varepsilon _2(t) l_BC} {a_{C/B} ^ n% = % %omega_2^2(t) l_BC} } right none

Velocity:

left lbrace { binom {V_C ^x % = % V_B ^x % + % V_{ C/B } ^x} {V_C ^y % = % V_B ^y % + % V_{ C/B } ^y} } right none

left lbrace { binom {V_C ^x % = % V_B sin%varphi_1(t) % + % V_{ C/B } sin%varphi_2(t)} {V_C ^y % = % V_B cos%varphi_1(t) % + % V_{ C/B } cos%varphi_2(t)} } right none

V_c % = % sqrt{ (V_c ^x)^2 % + % (V_c ^y)^2 } % = %

% = % sqrt{ V_B^2 [sin%varphi_1^2(t) % + % cos%varphi_1^2(t)] % + % 2V_B V_{ C/B } [ sin%varphi_1(t) sin%varphi_2(t) % + % cos%varphi_1(t) cos%varphi_2(t)]% + % V_{C/B}^2 [sin%varphi_2 ^2(t) % + % cos%varphi_2^2(t)] }

% = % sqrt{ V_B^2 % + % 2V_B V_{ C/B } cos(%varphi_1(t) - %varphi_2(t)) % + % V_{C/B}^2 }

Acceleration:

left lbrace { binom {a_C ^x % = % (a_B ^%tau)^x % + % (a_B ^n)^x % + % (a_{ C/B } ^%tau)^x % + % (a_{ C/B } ^n)^x} {a_C ^y % = % (a_B ^%tau)^y % + % (a_B ^n)^y % + % (a_{ C/B } ^%tau)^y % + % (a_{ C/B } ^n)^y} } right none

left lbrace { binom {a_C ^x % = % a_B ^%tau sin%varphi_1(t) % - % a_B ^n cos%varphi_1(t) % + % a_{ C/B } ^%tau sin%varphi_2(t) % - % a_{ C/B } ^n cos%varphi_2(t)} {a_C ^y % = % a_B ^%tau cos%varphi_1(t) % + % a_B ^n sin%varphi_1(t)% + % a_{ C/B } ^%tau cos%varphi_2(t) % + % a_{ C/B } ^n sin%varphi_2(t)} } right none

a_c % = % sqrt{ (a_c ^x)^2 % + % (a_c ^y)^2 } % = %

% = % left [ [(a_B ^%tau)^2 % + % (a_B ^n)^2 % + % (a_{C/B} ^%tau)^2 % + % (a_{C/B} ^n)^2][sin%varphi_1^2(t) % + % cos%varphi_1^2(t)] % + % (a_B ^%tau) (a_{C/B} ^%tau)[cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % (a_B ^%tau) (a_{C/B} ^n)[sin(%varphi_2(t) - %varphi_1(t))] % + % (a_B ^n) (a_{C/B} ^%tau)[sin(%varphi_1(t) - %varphi_2(t))] % + % (a_B ^n) (a_{C/B} ^n)[cos(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

% = % left [ [(a_B ^%tau)^2 % + % (a_B ^n)^2 % + % (a_{C/B} ^%tau)^2 % + % (a_{C/B} ^n)^2] % + % [a_B ^%tau a_{C/B} ^%tau % + % a_B ^n a_{C/B} ^n][cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % [a_B ^n a_{C/B} ^%tau % - % a_B ^%tau a_{C/B} ^n][sin(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

Conclusion
After substituting the linear velocities and accelerations with their angular variants, we obtain the following.

For any point from A to B (change l_AB accordingly):

V_B % = % %omega_1 l_AB

a_B % = % l_AB sqrt{ %varepsilon_1^2 % + % %omega_1^4 }

For any point from B to C (change l_BC accordingly) :

V_c % = % sqrt{ (%omega_1 l_AB)^2 % + % 2%omega_1 l_AB %omega_2 l_BC cos(%varphi_1(t) - %varphi_2(t)) % + % (%omega_2 l_BC)^2 }

a_c % = % left [ [(%varepsilon_1 l_AB)^2 % + % (%omega_1^2 l_AB)^2 % + % (%varepsilon_2 l_BC)^2 % + % (%omega_2^2 l_CB)^2] % + % [%varepsilon_1 l_AB %varepsilon_2 l_BC % + % %omega_1^2 l_AB %omega_2^2 l_BC][cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % [%omega_1^2 l_AB %varepsilon_2 l_BC % - % %varepsilon_1 l_AB %omega_2^2 l_BC][sin(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

%varphi_1 ( t ) A Force Analysis of Mechanical Finger

y

x
z
bar R_21 ^y

bar R_21 ^x
bar M'_R2

C B bar F

B bar P bar M_R2

%varphi_2 ( t ) bar B_1 bar B_2 bar M_R1

bar R_12 ^x

bar R_01 ^x bar R_12 ^y bar G_2

bar G_1
bar R_01 ^y

For the first element:
%SIGMA F_x: % % R_01 ^x + B_1 sin %varphi_1( t ) - R_21 ^x % = % 0

%SIGMA F_y: % % - R_01 ^y - G_1 - B_1 cos %varphi_1 ( t ) + R_21 ^y % = % 0

%SIGMA M_(A): - M_R1 - B_1 l_cm1 - G_1 cos %varphi_1 ( t ) l_cm1 + R_21^x sin %varphi_1 ( t ) l_AB + R_21^y sin %varphi_1 ( t ) l_AB + M'_R2 = 0

For the second element:
%SIGMA F_x: R_12 ^x + B_2 sin %varphi_2( t ) - P sin %varphi_2( t ) + Fcos %varphi_2(t) = 0

%SIGMA F_y: - R_12 ^y - G_2 - B_2 cos %varphi_2 ( t ) + P cos %varphi_2 ( t ) + F sin %varphi_2(t) = 0

%SIGMA M_(A): % % - M_R2 - B_2 l_cm2 - G_2 cos %varphi_2 ( t ) l_cm2 + P l_BC % = % 0

We have six unknowns ( R_01^x, R_01^y, R_12^x=R_21^x,R_12^y=R_21^y, M_R1, M_R2 = M'_R2 ) and six equations.

The equations need to be prepared for matrix form:

left lbrace alignl stack { R_01 ^x - R_21 ^x = - B_1 sin %varphi_1( t ) # - R_01 ^y + R_21 ^y = G_1 + B_1 cos %varphi_1 ( t ) # - M_R1 + R_21^x sin %varphi_1 ( t ) l_AB + R_21^y sin %varphi_1 ( t ) l_AB + M_r2 = B_1 l_cm1 + G_1 cos %varphi_1 ( t ) l_cm1 # R_12 ^x = - B_2 sin %varphi_2( t ) + P sin %varphi_2( t ) - F cos %varphi_2(t)# R_12 ^y = P cos %varphi_2 ( t ) - G_2 - B_2 cos %varphi_2 ( t ) + F sin %varphi_2(t) # M_R2 = P l_BC - B_2 l_cm2 - G_2 cos %varphi_2 ( t ) l_cm2 } right none
The final matrix form is as follows:

left[ matrix{1#0#-1#0#0#0##0#-1#0#1#0#0##0#0#sin %varphi_1(t) l_AB #sin %varphi_1(t) l_AB #-1#1##0#0#1#0#0#0##0#0#0#1#0#0##0#0#0#0#0#1 } right] left[ matrix{R_01^x##R_01^y##R_12^x##R_12^y##M_R1##M_R2 } right] = left[ matrix{- B_1 sin %varphi_1( t )## G_1 + B_1 cos %varphi_1 ( t )##B_1 l_cm1 + G_1 cos %varphi_1 ( t ) l_cm1##- B_2 sin %varphi_2( t ) + P sin %varphi_2( t ) - F cos %varphi_2(t)##P cos %varphi_2 ( t ) - G_2 - B_2 cos %varphi_2 ( t ) + F sin %varphi_2(t)##P l_BC - B_2 l_cm2 - G_2 cos %varphi_2 ( t ) l_cm2 } right]

The above system is now mathematically described and computer aided design may be implemented.

The angular positions, velocities and accelerations need to be read from the servo encoders in real time and fed into the matrix to apply proper control. Since our design lacks sensors, the forces P need to be determined before hand, based on the manipulated objects. This makes the system less robust and limited to picking up and moving only one object, say on a production line.

The reaction forces are calculated to properly obtain the moments of the motors. These moments are the counter balance moments, or torques, that need to be created and sustained by the motors to ensure proper functioning.

Without pressure sensors on the finger tips, designing any feedback controller for the hand is not feasible. Therefore we are forced to work with an open loop system that requires very precise calibration. It is imperative for the mathematical description of the system and its parameters to be as accurate as possible.

An immediate flaw of our analysis is the lack of friction forces working between the joints. The pressing force, and therefore the motor torque, needs to be overcompensated to ensure a proper grip.

Assumptions

The friction(F) and pressing(P) forces we see above are what hold our object in place. As mentioned, these need to be predetermined depending on the weight and size of the manipulated object. Therefore, the first assumptions that need to be made are its parameters. Let us assume our hand will be picking up a cube of a weight of 0.5kg and an appropriate size that depends on the length of the fingers.

We also need to assume the motion of the hand. If the hand is to simply pick up the object and place it down somewhere else we can limit its movement to one plane of motion. The hand then will be subjected to only four accelerations; upward, downward, left and right. The analysis for both horizontal accelerations are symmetrical, therefore they can be reduced to the analysis of only one direction. While the upward acceleration will be much more demanding on the hand than the downward acceleration (total acceleration = gravity +/- relative acceleration), therefore the downward acceleration may be omitted. This leaves us with only two necessary analysis:
-Vertical upward acceleration
-Horizontal acceleration

The next assumption that needs to be made is the driving method. The base of the fingers will be driven in pairs with a worm gear, while the finger tips will be driven independently also by worm
gears. The torque required to produce a given moment on the finger is as follows:

bar M_W left lbrace alignl {binom {P_{M_W} = 2 %pi M_W} {P_{ F } = Fp} } right none ,gives 2%pi M_W = pF

bar F
bar M_G	left lbrace alignl {binom {2%pi M_W = pF} {M_G = Fd} } right none

M_W = { M_G p } over { 2%pi d } , where alignl{binom{p - pitch}{ d - diameter of gear }}

These calculations are only an approximation as friction was omitted.

The final assumption to be made is the friction coefficient of the finger tip grip and object.

With the provided information, we are capable of preparing the Matlab code for our simulation and get a basic idea of the required motors and parts needed for the project. To not repeat ourselves, the Matlab code is provided at the end of the report. The only difference are the system parameters, now we only have assumptions to create a working prototype, were as the provided code contains the final system parameters for an accurate final analysis.